## Slide 1: IP Addressing

## Slide 2: IP Addressing
Logical addresses are 32 bits (4 bytes) long
  Each byte is represented as an octet (decimal number from 0 to 255)
  Usually represented in dotted decimal notation
    E.g., 172.24.208.192
  Address has two parts: network and host ID
    E.g. 172.24.208.192 (172.24.0.0 and 208.192)
  Categorized into ranges referred to as classes
    Class system provides basis for determining which part of address is the network and which is the host ID
    The first octet of an address denotes its class

## Slide 3: IP Addressing (continued)
Classes
  Class A: first octet between 1-126
    16,777,214 hosts per network address
  Class B: first octet between 128-191
    65,534 hosts per network address
  Class C: first octet between 192-223
    254 hosts per network address
  Class D: first octet between 224-239
    Reserved for multicasting
  Class E: first octet between 240-255
    Reserved for experimental use

## Slide 4: IP Addressing

## Slide 5: IP Addressing (continued)
127.0.0.0 network is called the loopback address
  localhost always corresponds to address 127.0.0.1
APIPA (Automatic Private IP Address)
  169.254.0.0/24 (class C address)
IETF reserved addresses for private networks
  Class A addresses beginning with 10
  Class B addresses from 172.16 to 172.31
  Class C addresses from 192.168.0 to 192.168.255
  These addresses can’t be routed across the Internet
  IPv6 eliminates need for private addressing; provides a 128-bit address (vs. IPv4’s 32 bits)

## Slide 6: Subnet Masks
Subnet mask determines which part of address denotes network portion and which denotes host
  32-bit number
  A binary 1 signifies that the corresponding bit in the IP address belongs to the network portion; a 0 signifies that bit in address belongs to host portion
  Default subnet mask uses a 255 in each octet in address that corresponds to the network portion
    Class A: 255.0.0.0
    Class B: 255.255.0.0
    Class C: 255.255.255.0